## Slide 1: Performance Tuning your Code: tight arithmetic, L1, L2 thrashing with 2D Arrays, and Alternate loops to enhance pipelining
David V. Beard

## Slide 2: Reading for CS 2275 Module 13
Lippman:
  17.2, 17.4, 12, A.3
Some of the notes and slides are from Bryant and O’Hallaron and from Null and Lobur

## Slide 3: Performance Tuning
Most computer architecture courses assume the computer scientist will be modifying the machine to match the code
  (more memory, faster CPI, etc)
In reality, the computer scientist generally as the get his or her code running as fast as needed on the particular machine at hand.
If the code is not sufficiently fast, it must be modified to run faster on that particular machine.
  Turn off the debugger
  Turn on the optimizer
  Where are the bottlenecks?
    95%/5% rule: 95% of the time is spent in 5% of the code
  Then use your knowledge of compliers & architecture to make the code faster

## Slide 4: Remember Don Knuth’s Quote:
(one of the key founders of computer science)
Premature optimization is the root of ALL Evil
  (https://en.wikiquote.org/wiki/Donald_Knuth)
If you make it faster, you generally make it more complex
One part of the system becomes more depending on another, leading to potential bugs over the years
KISS is always best unless you really need it faster.
  (Keep it simple stupid  )

## Slide 5: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 6: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of “locality of reference”, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Note: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that provides data to programs at the rate of the fast storage near the top.

## Slide 7: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 8: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 9: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 10: Examples of Caching in the Memory Hierarchy
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?

## Slide 11: Cache and Row v Col Major Access of 2D Arrays
2D array is really 1D array – generally “row major: order
Unsigned long long foo=
01 02 03 04 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 19 20 21 22 23 Actually stored in computer as 1D array:
foo = 01 02 03 04 05 06 07 08 09 10 12 13 14 15 16 17 18 19 20 21 22 23
foo[r][c] actually foo[r*#columns+c]
Note: each row is a single cache block. If I access all elements goi

## Slide 12: Cache & Row v Col Major Access of 2D Arrays
01 02 03 04 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 19 20 21 22 23
Note that each element is 8 bytes so each row is a 64byte cache block
Accessing each element going across the rows requirea 3 “cache hits”
However, going down the columns (01, 08, 16, 02, 09, 17, 03, …) requires hitting block 1, then block 2, then block 3, then block 1, then block 2, then block 3, ….
With a BIG array, you will not be able to hold enough blocks in L1 causing L1 Cache “Thrashing” or lots of “cache misses.”
With a REALLY BIG array, you can massively increase the number of misses and perhaps even page faults, requiring fetching pages from disk.

## Slide 13: Cache & Row v Col Major Access of 2D Arrays
const unsigned long long size= 10000;/or 10000000  unsigned long long *boo = new unsigned long long [size*size]; for(r=0;r<size;r++) for(c=0;c<size;c++) boo[r*size+c] = r+c;
Or alternatively:
for(c=0;c<size;c++) for(r=0;r<size;r++) boo[r*size+c] = r+c;

## Slide 14: clock
For exercise 13, we are going to time a number of different array sizes, methods of allocation, and row v col major access.
#include <ctime>
…
clock_t start = clock(); //instance of the clock_t class
cout << (double) ( clock() - start)/CLOCKS_PER_SEC << endl;
We will compare the built in rand() pseudo random number generator to a fast one I found on the internet:
  (no idea how good the pseudo random numbers are, but the code is interesting )
We will also compare the optimization settings on the gcc compiler

## Slide 15: Instruction Pipelining
Some CPUs divide the fetch-decode-execute cycle into smaller steps.
These smaller steps can often be executed in parallel to increase throughput.
Such parallel execution is called instruction pipelining.
Instruction pipelining provides for instruction level parallelism (ILP)
The next slide shows an example of instruction pipelining.

## Slide 16: Instruction Pipelining
Suppose a fetch-decode-execute cycle were broken into the following smaller steps:
Suppose we have a six-stage pipeline. S1 fetches the instruction, S2 decodes it, S3 determines the address of the operands, S4 fetches them, S5 executes the instruction, and S6 stores the result.
1. Fetch instruction. 4. Fetch operands.
2. Decode opcode. 5. Execute instruction.
3. Calculate effective 6. Store result.
address of operands.

## Slide 17: Instruction Pipelining
For every clock cycle, one small step is carried out, and the stages are overlapped.
S1. Fetch instruction. S4. Fetch operands.
S2. Decode opcode. S5. Execute.
S3. Calculate effective S6. Store result.
address of operands.

## Slide 18: Instruction Pipelining Speed Increases
Theoretically, a 5-pipeline architecture would allow 5 instructions to be completed at the same time, and thus would generate a factor-of-5 increase in speed.
However, that is not the case.
Pipeline hazards arise that cause pipeline conflicts and stalls. An instruction pipeline may stall, or be flushed for any of the following reasons:
  Resource conflicts.
  Data dependencies.
    Fetching an instruction from cashe, main memory, disk
  Conditional branching
    The instruction being calculated in the pipeline is never executed – rather another instruction needs to be executed that is not in the pipeline.
    Difficult to pipeline through some loops given the loop conditional

## Slide 19: Can we exploit pipelining to speed up code?
const unsigned long long size= 2000000000; unsigned long long i; unsigned long long *foo = new unsigned long long [size]; foo[0]=2;foo[1]=3;foo[2]=6; for(i = 3;i<size;i++) foo[i]=foo[i-1]+foo[i-2]-foo[i-3];
V.
foo[0]=3;foo[1]=3;foo[2]=6; for(i = 3; i<size-4;i+=4) { foo[i]=foo[i-1]+foo[i-2]-foo[i-3]; foo[i+1]=foo[i]+foo[i-1]-foo[i-2]; foo[i+2]=foo[i+1]+foo[i]-foo[i-1]; foo[i+3]=foo[i+2]+foo[i-1]-foo[i]; }